## Slide 1: Jonathan Swain Technical Director - NFU Energy
Taking the first steps towards Net Zero
Notes: Taking the first steps towards Net Zero
This last 12 months have seen much discussion about how Net Zero could be achieved, however much of this is aimed at changes taking place on the gas and electricity networks and less about practical steps that individuals can take. In this session Jon will explore what actions growers can take in the first steps towards reducing their carbon footprints and what the future may be for energy supply and consumption.

## Slide 3: So what is Net Zero?
I = CO2 emissions increasing the level of CO2 in the system
S = CO2 removals decreasing the level of CO2 in the system
Net Zero is when I=S
i.e. emissions into the system (inputs) are equal to emissions out of the system (sequestration)
The removal actions (S) are easier when emissions inputs (I) are lower
Gross Zero is when I=0
CO2

## Slide 4: Net Zero commitments

## Slide 5: The problem – emissions sources
Graph shows emissions makeup (orange and red)
Green is proposed action
First step is to reduce emissions
What can we influence in horticulture?
  Inputs
  Energy
  Productivity
  Transport

## Slide 6: Footsteps towards Net Zero
Measure
Understand
Reduce inputs
Be more efficient
Alternative resources
Sequester

## Slide 7: Footsteps towards Net Zero
Measure
Understand
Reduce inputs
Be more efficient
Alternative resources
Sequester

## Slide 8: Visualise emissions
1 tonne CO2e =
  4,000 kWh electricity – 4 MW lighting for 1 hour
  5,263 kWh gas burnt – 6 MW gas boiler for 53 minutes
  1,400 litres diesel – 700 miles in an HGV
  62.5 tonnes R401a refrigerant
  178 tonnes Ammonium Nitrate production

## Slide 9: Inputs – what carbon emissions?
Identify inputs - # per year
Set boundaries
Determine CO2 emissions - kg per #
  Ask supplier
  Calculate yourself
Create footprint
Ask ….
  Are they significant compared to other inputs
  What are the alternatives

## Slide 10: Emissions sources
Energy
Fertilisers
Pesticides
Plastics
Growing Media
Water
Wastes
Packaging
Etc.
Reduce
Recycle
Re-use

## Slide 11: Some good news – ‘natural’ decarbonisation
C. 200 gCO2e per kWh supplied electricity
Reductions from stopping burning coal
Reductions because of increasing renewable energy
Chart: Grid emissions factor
| year | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
gCO2e/kWh | 754.56 | 728.18 | 706.48 | 637.33 | 606.75 | 572.07 | 549.56 | 508.05 | 509.96 | 481.81 | 501.59 | 522.7 | 507.43 | 513.88 | 516.62 | 510.8 | 539.81 | 534.63 | 530.44 | 489.94 | 510.41 | 491.95 | 549.38 | 514.57 | 462.9 | 391.09 | 306.75 | 274.42 | 255.6

## Slide 12: Renewable electricity
Renewables account for 76% of electricity generation
Notes: Less important to growers but shows the direction of travel
National Grid Future Energy Scenarios show how heating could be electricfied
Gas is only as big as Solar
Additional 3 GW of wind power suggested

## Slide 13: The effect
Chart: 
| 2000 | 2010 | 2018 | 2050
Carbon emissions for 5Ha nursery's elec consumption | 467.9159 | 476.1437 | 238.4403 | 18.6573

## Slide 14: Heating fuels - Less good news
Gas and oil based heating fuels c. 190 – 220 gCO2e per kWh
Unlikely to change much
  Small biomethane influence
  Possible hydrogen blend in the future <20%
How else to decarbonise heat in horticulture??
  CHP
  Heat Pumps
  Biomass

## Slide 15: Heat Pumps – decarbonisation at work
1 kWh heat from gas network = 211 g CO2 - 238 g CO2
1 kWh heat delivered by heat pump = 40 g CO2 – 67 g CO2
  Current grid electricity emissions are 200 g CO2 /kWh
  As grid electricity decarbonises further, heat pump emissions fall
Notes: We should understand the reason for the drive to heat pumps
Carbon savings are huge (it’s solar energy after all)
We may have to compromise on temperatures

## Slide 16: Examples
Chart: Tonnes CO2 emitted per year - 5Ha unlit glasshouse
| Mains gas old boiler and elec | Mains gas new boiler and elec | Efficient CHP | Mains elec - heat pump | Biomas and mains elec
 | 6117.478 | 4810.9008 | 4305.4361 | 1549.7658 | 453.8288
Chart: Tonnes CO2 emitted per year - 5Ha lit glasshouse
| Mains gas old boiler and elec | Mains gas new boiler and elec | Efficient CHP | Mains elec - heat pump | Biomas and mains elec
 | 14634.9904 | 12414.5726 | 11555.5779 | 6872.5484 | 5010.0959

## Slide 17: Policy drives
Positive drivers
  RHI Extension
  New Tariff Guarantees
  Green Gas Support Scheme
  Renewable Heat Grants
  Green Heat Network Fund
  Energy Innovation Fund
  CCL/CCA extension
Disincentives to use fossil fuels
  Increasing CCL Charges
  Green Gas Levy
  Carbon Price application
Notes: https://ahdb.org.uk/growsave-budget-news
The positives are more numerous than the negatives BUT their likely impact is smaller
Trajectory was set pre Covid

## Slide 18: The 10 point plan…
40 GW offshore wind
5 GW Hydrogen
Nuclear
Electric Vehicles
Public transport and cycling/walking
Jet Zero and green maritime
More efficient homes and public buildings
Carbon capture of 10 million tonnes
30,000 Ha tree planting?
London the centre of green finance

## Slide 19: Decarbonising heat is the future
Heat sources are not just the ground or ground water…
Biomass has an important part to play
However, don’t forget the CO2 enrichment challenge
Notes: We should understand the reason for the drive to heat pumps
Carbon savings are huge (it’s solar energy after all)
We may have to compromise on temperatures

## Slide 20: Carbon capture
£350m package of funding announced 22 July 2020
  Nothing specifically for horticulture, but…
  Aiming for transition from Gas to Hydrogen
  Scaling up Carbon Capture and Storage technologies including Direct Air Capture
Notes: Covid didn’t really change this but gave it a platform
We’re not just interested in reducing emissions but removing carbon too – essential for Net Zero
Hydrogen in the gas network…less CO2 for enrichment
https://www.gov.uk/government/news/pm-commits-350-million-to-fuel-green-recovery
https://www.drax.com/about-us/our-projects/bioenergy-carbon-capture-use-and-storage-beccs/

## Slide 21: Consequential effects – e.g. refrigeration
Don’t forget indirect emissions
  Manufacture
  Disposal
  Increased energy consumption?!
Refrigerant | GWP CO2e direct emissions
404A | 3922
434A | 3245
422A | 3143
407C | 1774
152A | 124
CO2 | 1
Ammonia | 0

## Slide 22: So what does it all mean?
Energy is an important CO2 emission to tackle
Renewable electricity will soon dominate at grid and user levels
Greenhouse heating is moving towards heat pumps for new build and some retrofit
New sources of CO2 need to be found to replace gas burning
Input efficiency is really important to reduce emissions at source
Reduced consumption
Renewable energy
Re-use resources

## Slide 23
Questions?